## Slide 1: Chapter 3: Campus Network Architecture
CCNP SWITCH: Implementing Cisco IP Switched Networks
Notes: Cisco Networking Academy Program
CCNP ROUTE: Implementing IP Routing
Chapter 1: Routing Services

## Slide 2: Chapter 3 Objectives
Implementing VLANs and trunks in campus switched architecture
Understanding the concept of VTP and its limitation and configurations
Implementing and configuring EtherChannel
Notes: Chapter 1 Objectives

## Slide 3: Implementing VLANs and Trunks in Campus Environment

## Slide 4: Implementing VLANs and Trunks in Campus Environment
Within the switched internetwork, VLANs provide segmentation and organizational flexibility.
VLANs help administrators to have the end node or workstations group that are segmented logically by functions, project teams, and applications, without regard to the physical location of the users.
VLANs allow you to implement access and security policies to particular groups of users and limit the broadcast domain.
The voice VLAN feature enables access ports to carry IP voice traffic from an IP phone. Because the sound quality of an IP phone call can deteriorate if the data is unevenly sent, the switch supports quality of service (QoS).

## Slide 5: VLAN Overview

## Slide 6: VLAN Segmentation
Larger flat networks generally consist of many end devices in which broadcasts and unknown unicast packets are flooded on all ports in the network.
One advantage of using VLANs is the capability to segment the Layer 2 broadcast domain. All devices in a VLAN are members of the same broadcast domain. If an end device transmits a Layer 2 broadcast, all other members of the VLAN receive the broadcast.
Switches filter the broadcast from all the ports or devices that are not part of the same VLAN.
In a campus design, a network administrator can design a campus network with one of two models:
  End-to-End VLANs
  Local VLANs.
Each model has its own advantages and disadvantages.

## Slide 7: End-to-End VLANs
End-to-End VLAN refers to a single VLAN that is associated with switch ports widely dispersed throughout an enterprise network on multiple switches.

## Slide 8: End-to-End VLAN Model Characteristics
Each VLAN is dispersed geographically throughout the network.
Users are grouped into each VLAN regardless of the physical location.
As a user moves throughout a campus, the VLAN membership of that user remains the same, regardless of the physical switch to which this user attaches.
Users are typically associated with a given VLAN for network management reasons. This is why they are kept in the same VLAN, therefore the same group, as they move through the campus.
All devices on a given VLAN typically have addresses on the same IP subnet.
Switches commonly operate in a server/client VTP mode.

## Slide 9: Local VLANs
In a local VLAN model, all users of a set of geographically common switches are grouped into a single VLAN, regardless of the organizational function of those users.

## Slide 10: Local VLAN Model Characteristics
The network administrator should create local VLANs with physical boundaries in mind rather than the job functions of the users on the end devices.
Generally, local VLANs exist between the access and distribution levels.
Traffic from a local VLAN is routed at the distribution and core levels to reach destinations on other networks.
Configure the VTP mode in transparent mode because VLANs on a given access switch should not be advertised to all other switches in the network, nor do they need to be manually created in any other switch VLAN databases.
A network that consists entirely of local VLANs can benefit from increased convergence times offered via routing protocols, instead of a spanning tree for Layer 2 networks. It is usually recommended to have one to three VLANs per access layer switch.

## Slide 11: Comparison of End-to-End VLANs and Local VLANs
Reasons for implementing the end-to-end design:
Grouping users
  Users can be grouped on a common IP segment, even though they are geographically dispersed.
Security
  A VLAN can contain resources that should not be accessible to all users on the network, or there might be a reason to confine certain traffic to a particular VLAN.
Applying quality of service (QoS)
  Traffic can be a higher- or lower-access priority to network resources from a given VLAN.

## Slide 12: Comparison of End-to-End VLANs and Local VLANs
Reasons for implementing the end-to-end design (cont.):
Routing avoidance
  If much of the VLAN user traffic is destined for devices on that same VLAN.
Special-purpose VLAN
  Sometimes a VLAN is provisioned to carry a single type of traffic that must be dispersed throughout the campus (for example, multicast, voice, or visitor VLANs).
Poor design
  For no clear purpose, users are placed in VLANs that span the campus or even span WANs. Sometimes when a network is already configured and running, organizations are hesitant to improve the design because of downtime or other political reasons.

## Slide 13: Comparison of End-to-End VLANs and Local VLANs
Reasons for implementing the Local Vlan design:
Deterministic traffic flow
  The simple layout provides a predictable Layer 2 and Layer 3 traffic path.
Active redundant paths
  When implementing Per-VLAN Spanning Tree (PVST) or Multiple Spanning Tree (MST) because there is no loop, all links can be used to make use of the redundant paths.
High availability
  Redundant paths exist at all infrastructure levels.
Finite failure domain
  If VLANs are local to a switch block, and the number of devices on each VLAN is kept small, failures at Layer 2 are confined to a small subset of users.
Scalable design
  Following the enterprise campus architecture design, new access switches can be easily incorporated, and new submodules can be added when necessary.
Notes: Local VLAN traffic on access switches can be passed to the building distribution switches across an alternative Layer 2 path if a primary path failure occurs. Router redundancy protocols can provide failover if the default gateway for the access VLAN fails. When both the STP instance and VLAN are confined to a specific access and distribution block, Layer 2 and Layer 3 redundancy measures and protocols can be configured to failover in a coordinated manner.

## Slide 14: Comparison of End-to-End VLANs and Local VLANs
End-to-End VLANs drawbacks:
Switch ports are provisioned for each user and associated with a given VLAN. Because users on an end-to-end VLAN can be anywhere in the network, all switches must be aware of that VLAN. This means that all switches carrying traffic for end-to-end VLANs are required to have those specific VLANs defined in each switch’s VLAN database.
Flooded traffic for the VLAN is, by default, passed to every switch even if it does not currently have any active ports in the particular end-to-end VLAN.
Troubleshooting devices on a campus with end-to-end VLANs can be challenging because the traffic for a single VLAN can traverse multiple switches in a large area of the campus, and that can easily cause potential spanning-tree problems.

## Slide 15: Implementing a Trunk in a Campus Environment
A trunk is a point-to-point link that carries the traffic for multiple VLANs across a single physical link between the two switches or any two devices.
Trunking is used to extend Layer 2 operations across an entire network.

## Slide 16: Trunking Protocols
A special protocol is used to carry multiple VLANs over a single link between two devices.
There are two trunking technologies:
Inter-Switch Link (ISL): A Cisco proprietary trunking encapsulation
IEEE 802.1Q: An industry-standard trunking method

## Slide 17: ISL Frame

## Slide 18: 802.1Q Frame

## Slide 19: IEEE 802.1Q/802.1p advantages over ISL
802.1Q has smaller frame overhead than ISL. As a result, 802.1Q is more efficient than ISL, especially in the case of small frames. 802.1Q overhead is 4 bytes, whereas ISL is 30 bytes.
802.1Q is a widely supported industry standard protocol.
802.1Q has the support for 802.1p fields for QoS.

## Slide 20: 802.1Q tag
Inserted 802.1Q tag (4 bytes, detailed here)
  EtherType(TPID): Set to 0x8100 to specify that the 802.1Q tag follows.
  PRI: 3-bit 802.1p priority field.
  CFI: Canonical Format Identifier is always set to 0 for Ethernet switches and to 1 for Token Ring-type networks.
  VLAN ID: 12-bit VLAN field. Of the 4096 possible VLAN IDs, the maximum number of possible VLAN configurations is 4094. A VLAN ID of 0 indicates priority frames, and value 4095 (FFF) is reserved.
Notes: If a non-802.1Q-enabled device or an access port receives an 802.1Q frame, the tag data is ignored, and the packet is switched at Layer 2 as a standard Ethernet frame. This allows for the placement of Layer 2 intermediate devices, such as unmanaged switches or bridges, along the 802.1Q trunk path. To process an 802.1Q tagged frame, a device must enable a maximum transmission unit (MTU) of 1522 or higher.
Baby giants are frames that are larger than the standard MTU of 1500 bytes but less than 2000 bytes. Because ISL and 802.1Q tagged frames increase the MTU beyond 1500 bytes, switches consider both frames as baby giants. ISL-encapsulated packets over Ethernet have an MTU of 1548 bytes, whereas 802.1Q has an MTU of 1522 bytes.

## Slide 21: Understanding Native VLAN in 802.1Q Trunking
A frequent configuration error is to have different native VLANs. The native VLAN that is configured on each end of an 802.1Q trunk must be the same.
Cisco switches use Cisco Discovery Protocol (CDP) to warn of a native VLAN mismatch
By default, the native VLAN will be VLAN 1.
Switch(config-if)# switchport trunk native vlan vlan-id
Notes: Note Cisco ISL does not have a concept of native VLAN. Traffic for all VLANs is tagged by encapsulating each frame.

## Slide 22: Understanding DTP

## Slide 23: DTP Modes Combination

## Slide 24: VLAN Ranges and Mappings
ISL supports VLAN numbers in the range of 1 to 1005, whereas 802.1Q VLAN numbers are in the range of 1 to 4094.
The default behavior of VLAN trunks is to permit all normal and extended-range VLANs across the link if it is an 802.1Q interface and to permit normal VLANs in the case of an ISL interface.

## Slide 25: Supported VLAN on Catalyst Switchs

## Slide 26: VLAN Ranges

## Slide 27: Configuring, Verifying, and Troubleshooting VLANs and Trunks
Step 1. Enter global configuration mode:
  Switch# configure terminal
Step 2. Create a new VLAN with a particular ID number:
  Switch(config)# vlan vlan-id
Step 3. (Optional.) Name the VLAN:
  Switch(config-vlan)# name vlan-name

## Slide 28: Assigning an Access Port to a VLAN
Step 1. From global configuration mode, enter the configuration mode for the particular port you want to add to the VLAN:
  Switch(config)# interface interface-id
Step 2. Specify the port as an access port:
  Switch(config-if)# switchport mode access
  Switch(config-if)# switchport host
Step 3. Remove or place the port in a particular VLAN:
  Switch(config-if)# [ no ] switchport access vlan vlan-id
Notes: Note The switchport host command effectively configures a port for a host device, such as a workstation or server. This feature is a macro for enabling spanning-tree PortFast and disabling EtherChanneling on a per-port basis. These features are discussed in later chapters. The switchport mode access command is needed so that the interface doesn’t attempt to negotiate trunking.

## Slide 29: Assigning an Access Port to a VLAN

## Slide 30: Verifying the VLAN Configuration

## Slide 31: Verifying the VLAN Configuration

## Slide 32: Displaying Information About the Interface

## Slide 33: Displaying Detailed Switch Port Information

## Slide 34: Displaying MAC Address Table Information

## Slide 35: Topology to Configure VLAN and Trunking

## Slide 36: Configuring VLANs and Trunks
Step 1. Create VLAN 20 on both switches.
  SW1(config)# vlan 20
  SW1(config-vlan)# exit
  % Applying VLAN changes may take few minutes. Please wait...
Step 2. On SW1/2 configure port Ethernet 0/2 to be an access port and assign it to VLAN 20
  SW1(config)# interface ethernet 0/2
  SW1(config-if)# switchport mode access
  SW1(config-if)# switchport access vlan 20
Step 3. Configure ports that connect SW1 and SW2 as trunks. Use the dot1Q encapsulation.
  Trunk configuration on SW1:
  SW1(config)# interface Ethernet 1/1
  SW1(config-if)# switchport trunk encapsulation dot1q
  SW1(config-if)# switchport trunk allowed vlan 1,20
  SW1(config-if)# switchport mode trunk
  Trunk configuration on SW2:
  SW2(config)# interface Ethernet 1/2
  SW2(config-if)# switchport trunk encapsulation dot1q
  SW2(config-if)# switchport trunk allowed vlan 1,20
  SW2(config-if)# switchport mode trunk

## Slide 37: Verify Trunking

## Slide 38: Best Practices for VLANs and Trunking
For the Local VLANs model, it is usually recommended to have only one to three VLANs per access module.
Avoid using VLAN 1 as the black hole for all unused ports.
Try to always have separate voice VLANs, data VLANs, management VLANs, native VLANs, black hole VLANs, and default VLANs (VLAN 1).
In the local VLANs model, avoid VTP; it is feasible to use manually allowed VLANs in a network on trunks.
For trunk ports, turn off DTP and configure it manually.
Use IEEE 802.1Q rather than ISL because it has better support for QoS and is a standard protocol.
Manually configure access ports that are not specifically intended for a trunk link.
Prevent all data traffic from VLAN 1; only permit control protocols to run on VLAN 1 (DTP, VTP, STP bridge protocol data units [BPDUs], Port Aggregation Protocol [PAgP], Link Aggregation Control Protocol [LACP], Cisco Discovery Protocol [CDP], and such.).
Avoid using Telnet because of security risks; enable Secure Shell (SSH) support on management VLANs.

## Slide 39: Best Practices for VLANs and Trunking
DTP is useful when the status of the switch on the other end of the link is uncertain or might be changing over time. When the link is to be set to trunk in a stable manner, changing both ends to trunk nonegotiate accelerates the convergence time, saving up to 2 seconds upon boot time. We recommend this mode on stable links between switches that are part of the same core infrastructure.
On trunk links, it is recommended to manually prune the VLANs that are not used.
It is also a good practice to have an unused VLAN as a native VLAN on the trunk links to prevent DTP spoofing.
If trunking is not used on a port, you can disable it with the interface level command switchport host .

## Slide 40: Voice VLAN Overview
Multiservice switches support a new parameter for IP telephony support that makes the access port a multi-VLAN access port.
The new parameter is called a voice or auxiliary VLAN . Every Ethernet 10/100/1000 port in the switch is associated with two VLANs:
  A native VLAN for data service that is identified by the PVID
  A voice VLAN that is identified by the voice VLAN ID (VVID)
During the initial CDP exchange with the access switch, the IP phone is configured with a VVID.
The IP phone is also supplied with a QoS configuration using CDP.

## Slide 41: Voice VLAN Overview

## Slide 42: Switch Configuration for Wireless Network Support
Cisco offers the following two WLAN implementations:
  The standalone WLAN solution is based on autonomous (standalone) access points (APs).
  The controller-based WLAN solution is based on controller-based APs and WLCs (Wireless LAN Controllers).

## Slide 43: Autonomous WLAN
In the autonomous (or standalone) solution, each AP operates independently and acts as a transition point between the wireless media and the 802.3 media.
The data traffic between two clients flows via the Layer 2 switch when on the same subnet from a different AP infrastructure. As the AP converts the IEEE 802.11 frame into an 802.3 frame, the wireless client MAC address is transferred to the 802.3 headers and appears as the source for the switch.
The destination, also a wireless client, appears as the destination MAC address.

## Slide 44: Controller-Based WLAN
In a controller-based solution, management, control, deployment, and security functions are moved to a central point: the wireless controller.
To implement a wireless network, APs and switches need to be configured. APs can be configured directly (autonomous APs) or through a controller (lightweight APs).
Either way, configuring APs is a domain of the WLAN specialist. On the switch side, just configure VLANs and trunks on switches to support WLAN.

## Slide 45
VLAN Trunking Protocol

## Slide 46: VLAN Trunking Protocol
VTP overview
VTP modes
VTP versions
VTP pruning
VTP authentication
VTP advertisements
VTP configuration and verifications
VTP configuration overwriting
VTP best practices

## Slide 47: VTP Overview
VTP is a Layer 2 protocol that maintains VLAN configuration consistency by managing the additions, deletions, and name changes of VLANs across networks
Switches transmit VTP messages only on 802.1Q or ISL trunks.
Cisco switches transmit VTP summary advertisements over the management VLAN (VLAN 1 by default) using a Layer 2 multicast frame every 5 minutes.
VTP domain is one switch or several interconnected switches sharing the same VTP environment but switch can be only in one VTP domain at any time.
By default, a Cisco Catalyst switch is in the no-management-domain state or <null> until it receives an advertisement for a domain over a trunk link or until you configure a management domain.
Configurations that are made on a single VTP server are propagated across trunk links to all of the connected switches in the network.
Configurations will be exchanged if VTP domain and VTP passwords match.
VTP is a Cisco proprietary protocol.

## Slide 48: VTP Propagation
Step 1. An administrator adds a new VLAN definition.
Step 2. VTP propagates the VLAN information to all switches in the VTP domain.
Step 3. Each switch synchronizes its configuration to incorporate the new VLAN data.

## Slide 49: VTP Modes
Notes: Server: The default VTP mode is server mode, but VLANs are not propagated over the network until a management domain name is specified or learned. When you make a change to the VLAN configuration on a VTP server, the change is propagated to all switches in the VTP domain. VTP messages are transmitted out of all the trunk connections.
Transparent: When you make a change to the VLAN configuration in VTP transparent mode, the change affects only the local switch. The change does not propagate to other switches in the VTP domain. VTP transparent mode does forward VTP advertisements that it receives within the domain.
Client: A VTP client behaves like a VTP server and transmits and receives VTP updates on its trunks, but you cannot create, change, or delete VLANs on a VTP client. VLANs are configured on another switch in the domain that is in server mode.

## Slide 50: VTP Operation
By default, Cisco IOS VTP servers and clients save VLANs to the vlan.dat file in flash memory, causing them to retain the VLAN table and revision number.
The erase startup-config command does not affect the vlan.dat file on switches in VTP client and server modes.
Switches that are in VTP transparent mode display the VLAN and VTP configurations in the show running-config command output because this information is stored in the configuration text file.
If you perform erase startup-config on a VTP transparent switch you will delete its VLANs.

## Slide 51: VTP Versions
Cisco Catalyst switches support three different versions of VTP: 1, 2, and 3.
It is importante to decide which version to use because they are not interoperable.
Cisco recommends running only one VTP version for network stability.
The default VTP version that is enabled on a Cisco switch is Version 1.
If you do need to change the version of VTP in the domain, the only thing that you need to do is to enable it on the VTP server; the change will propagate throughout the network.

## Slide 52: VTP Version 1 and 2
Version-dependent transparent mode
  VTP Version 1, a VTP transparent network device inspects VTP messages for the domain name and version
  VTP Version 2 forwards VTP messages in transparent mode, without checking the version.
Consistency check
  In VTP Version 2, VLAN consistency checks, such as VLAN names and values, are performed.
Token ring support
  VTP Version 2 supports Token Ring LAN switching and VLANs.
Unrecognized type-length-value support
  VTP Version 2 switches propagate received configuration change messages out other trunk links, even if they are not able to understand the message.
Notes: Consistency check
  In VTP Version 2, VLAN consistency checks, such as VLAN names and values, are performed. However, this is only done when you enter information through the command-line interface (CLI) or Simple Network Management Protocol (SNMP). Consistency checks are not performed when new information is obtained from a VTP message or when information is read from NVRAM. If the digest on a received VTP message is correct, its information is accepted without consistency checks.

## Slide 53: VTP Version 3
Extended VLAN support
  VTP also can be used to propagate extended VLANs
Domain name is not automatically learned
  With VTPv2, a factory default switch that receives a VTP message will adapt the new VTP domain name.
Better security
  VTP domain password is secure during transmission and in the switch’s database.
Better database propagation.
  Only the primary server is allowed to update other devices and only one server per VTP domain is allowed to have this role.
Multiple Spanning Tree (MST) support
  VTPv3 adds support for propagation of MST instances.

## Slide 54: VTP Pruning

## Slide 55: VTP Authentication
VTP domains can be secured by using the VTP password feature.
It is important to make sure that all the switches in the VTP domain have the same password and domain name; otherwise, a switch will not become a member of the VTP domain.
Cisco switches use the message digest 5 (MD5) algorithm to encode passwords in 16-byte words.
These passwords propagate inside VTP summary advertisements.
In VTP, passwords are case sensitive and can be 8 to 64 characters in length.
The use of VTP authentication is a recommended practice.

## Slide 56: VTP Advertisements

## Slide 57: VTP Messages Types
Summary Advertisements
  By default, Catalyst switches issue summary advertisements in 5-minute increments. Summary advertisements inform adjacent Catalysts of the current VTP domain name and the configuration revision number.
  When the switch receives a summary advertisement packet, the switch compares the VTP domain name to its own VTP domain name.
  If the name differs, the switch simply ignores the packet.
  If the name is the same, the switch then compares the configuration revision to its own revision.
  If its own configuration revision is higher or equal, the packet is ignored. If it is lower, an advertisement request is sent.

## Slide 58: VTP Messages Types
Subset Advertisements
  When you add, delete, or change a VLAN in a Catalyst server, the Catalyst server where the changes are made increments the configuration revision and issues a summary advertisement.
  One or several subset advertisements follow the summary advertisement.
  A subset advertisement contains a list of VLAN information.
Advertisement Requests are sent when:
  The switch has been reset.
  The VTP domain name has been changed.
  The switch has received a VTP summary advertisement with a higher configuration revision than its own.
  Upon receipt of an advertisement request, a VTP device sends a summary advertisement. One or more subset advertisements follow the summary advertisement.

## Slide 59: Configuring and Verifying VTP
Step 1. Configure VTP on all the switches, Switch 1 and Switch 3 as client mode where as Switch2 as server mode

## Slide 60: Overwriting VTP Configuration (Very Common Issue with VTP)

## Slide 61: Overwriting VTP Configuration (Very Common Issue with VTP)

## Slide 62: Overwriting VTP Configuration (Very Common Issue with VTP)

## Slide 63: VTP Key Points
Avoid, as much as possible, VLANs that span the entire network.
The VTP revision number is stored in NVRAM and is not reset if you erase the switch configuration and reload it. To reset the VTP revision number to zero, use the following two options:
  Change the switch’s VTP domain to a nonexistent VTP domain, and then change the domain back to the original name.
  Change the switch’s VTP mode to transparent and then back to the previous VTP mode.

## Slide 64: Best Practices for VTP Implementation
VTP is often used in a new network to facilitate the implementation of VLANs.
However, as the network grows larger, this benefit can turn into a liability.
If a VLAN is deleted by accident on one server, it is deleted throughout the network.
If a switch that already has a VLAN database defined is inserted into the network, it can hijack the VLAN database by deleting added VLANs.
Because of this, it is the recommended practice to configure all switches to transparent VTP mode and manually add VLANs as needed, especially in a larger campus network.
VTP configuration is usually good for small environments.

## Slide 65
Implementing EtherChannel in a Switched Network

## Slide 66: Implementing EtherChannel in a Switched Network
The need for EtherChannel technology
Port aggregation negotiation protocols
Configuration steps for bundling interfaces into a Layer 2 EtherChannel
Configuring EtherChannel
Changing EtherChannel load-balancing behavior
How EtherChannel load-balancing works
The role of EtherChannel Guard

## Slide 67: The Need for EtherChannel

## Slide 68: EtherChannel Overview
EtherChannel is a technology that was originally developed by Cisco as a LAN switchto- switch technique of grouping several Fast or Gigabit Ethernet ports into one logical channel.
This technology has many benefits:
  It relies on the existing switch ports. There is no need to upgrade the switch-to-switch link to a faster and more expensive connection.
  Most of the configuration tasks can be done on the EtherChannel interface instead of on each individual port, thus ensuring configuration consistency throughout the switch-to-switch links.
  Load balancing is possible between the links that are part of the same EtherChannel. Depending on the hardware platform, you can implement one or several methods, such as source-MAC to destination-MAC or source-IP to destination-IP load balancing across the physical links.
Notes: Note Using new technologies like VSS (Virtual Switching System) and vPC (Virtual Port Channel), a port channel can be created across two aggregation switches from the same access layer to provide better redundancy.

## Slide 69: EtherChannel Mode Interactions
EtherChannel can be established using one of the following three mechanisms:
  LACP: IEEE’s negotiation protocol
  PAgP: Cisco’s negotiation protocol
  Static persistence: No negotiation protocol

## Slide 70: LACP
Link Aggregation Control Protocol (LACP) is part of an IEEE specification (802.3ad) that allows several physical ports to be bundled together to form a single logical channel. LACP allows a switch to negotiate an automatic bundle by sending LACP packets to the peer.
It ensures that when EtherChannel is created, all ports have the same type of configuration speed, duplex setting, and VLAN information. Any port modification after the creation of the channel will also change all the other channel ports.
The switch with the lowest system priority is allowed to make decisions about what ports actively participate in EtherChannel.

## Slide 71: LACP
Ports become active according to their port priority.
A lower number means higher priority.
Commonly up to 16 links can be assigned to an EtherChannel, but only 8 can be active at a time.
Nonactive links are placed into a standby state and are enabled if one of the active links goes down.
The maximum number of active links in an EtherChannel varies between switches.

## Slide 72: LACP Modes of Operation
These are the LACP modes of operation:
Active: Enable LACP
Passive: Enable LACP only if an LACP device is detected
The following are some additional parameters that you can use when configuring LACP:
System priority
  Each switch running LACP must have a system priority. The system priority can be specified automatically or through the CLI. The switch uses the MAC address and the system priority to form the system ID.
Port priority
  Each port in the switch must have a port priority. The port priority can be specified automatically or through the CLI.
Administrative key
  Each port in the switch must have an administrative key value, which can be specified automatically or through the CLI. The administrative key defines the capability of a port to aggregate with other ports, determined by these factors: the port’s physical characteristics, such as data rate, duplex capability, and point-to-point or shared medium.
Notes:   The port priority and the port number form the port identifier. The switch uses the port priority to decide which ports to put in standby mode when a hardware limitation prevents all compatible ports from aggregating.

## Slide 73: PAgP
Port Aggregation Protocol (PAgP) provides the same negotiation benefits as LACP.
PAgP is a Cisco proprietary protocol, and it will work only on Cisco devices.
PAgP packets are exchanged between switches over EtherChannel-capable ports.
Neighbors are identified and capabilities are learned and compared with local switch capabilities.
Ports that have the same capabilities are bundled together into an EtherChannel.
PAgP forms an EtherChannel only on ports that are configured for identical VLANs or trunking.
PAgP will automatically modify parameters of the EtherChannel if one of the ports in the bundle is modified.
PAgP and LACP are not compatible.
Notes: For example, if configured speed, duplex, or VLAN of a port in a bundle is changed, PAgP reconfigures that parameter for all ports in the bundle.

## Slide 74: PAgP Modes of Operation
These are the following two PAgP modes of operation:
■ Desirable: Enable PAgP
■ Auto: Enable PAgP only if a PAgP device is detecte

## Slide 75: Statically Bundle Links
Negotiation with either LACP or PAgP introduces overhead and delay in initialization.
As an alternative, you can statically bundle links into an EtherChannel.
This method introduces no delays but can cause problems if not properly configured on both ends.

## Slide 76: Layer 2 EtherChannel Configuration Guidelines
Before implementing EtherChannel in a network, plan the following steps necessary to make it successful:
The first step is to identify the ports that you will use for the EtherChannel on both switches.
Each interface should have the appropriate protocol identified (PAgP or LACP), have a channel group number to associate all the given interfaces with a port group, and be configured whether negotiation should occur.
After the connections are established, make sure that both sides of the EtherChannel have formed and are providing aggregated bandwidth.

## Slide 77: Layer 2 EtherChannel Configuration Guidelines
Follow these guidelines and restrictions when configuring EtherChannel interfaces:
EtherChannel support
  All Ethernet interfaces on all modules support EtherChannel, with no requirement that interfaces be physically contiguous or on the same module.
Speed and duplex
  Configure all interfaces in an EtherChannel to operate at the same speed and in the same duplex mode.
VLAN match
  All interfaces in the EtherChannel bundle must be assigned to the same VLAN or be configured as a trunk.
Range of VLANs
  An EtherChannel supports the same allowed range of VLANs on all the interfaces in a trunking Layer 2 EtherChannel.

## Slide 78: Layer 2 EtherChannel Configuration Guidelines
STP path cost
  Interfaces with different STP port path costs can form an EtherChannel as long as they are compatibly configured.
  Setting different STP port path costs does not, by itself, make interfaces incompatible for the formation of an EtherChannel.
Port channel versus interface configuration
  After you configure an EtherChannel, any configuration that you apply to the port channel interface affects the EtherChannel.
  Any configuration that you apply to the physical interfaces affects only the specific interface that you configured.

## Slide 79: EtherChannel Load-Balancing Options
Notes: To verify load-balancing options available on the device, use the port-channel loadbalance ? global configuration command.
Note Default configuration can differ from switch to switch, but commonly the default option is src-dst-ip. It is not possible to have different load-balancing methods for different EtherChannels on one switch. If the load-balancing method is changed, it is applicable for all EtherChannels.

## Slide 80: Configuring EtherChannel in a Switched Network

## Slide 81: Configuring EtherChannel in a Switched Network
Step 1.
Configure the two ports that connect each switch to use channel group 1 and LACP active mode:
Switch1# configure terminal
Switch1(config)# interface range Ethernet 1/1-2
Switch1(config-if-range)# channel-group 1 mode active
Creating a port-channel interface Port-channel 1
Step 2.
Enter interface configuration mode for the newly created port channel interface and configure it for trunk mode using dot1Q:
Switch1(config)# interface port-channel 1
Switch1(config-if)# switchport trunk encapsulation dot1q
Switch1(config-if)# switchport mode trunk

## Slide 82: Configuring EtherChannel in a Switched Network
Step 3.
On Switch 1, enter the show etherchannel summary command:

## Slide 83: Configuring EtherChannel in a Switched Network
Step 4.
Enter the show etherchannel load-balance command to verify which information EtherChannel uses to load balance traffic:

## Slide 84: Chapter 3 Summary
Implementing VLANs and trunks in campus switched architecture
Understanding the concept of VTP and its limitation and configurations
Implementing and configuring EtherChannel

## Slide 85: Chapter 3 Labs
CCNPv7.1 SWITCH Lab3.1 VLAN TRUNK VTP
CCNPv7.1 SWITCH Lab3.2 ETHERCHANNEL

## Slide 87: Acknowledgment
Some of the images and texts are from Implementing Cisco IP Switched Networks (SWITCH) Foundation Learning Guide: (CCNP SWITCH 300-115) by Richard Froom and Erum Frahim (1587206641)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva