## Slide 1: Chapter 4: Spanning Tree in Depth
CCNP SWITCH: Implementing Cisco IP Switched Networks

## Slide 2: Chapter 4 Objectives
Spanning Tree Protocol (STP) overview, its operations, and history
Implement Rapid Spanning Tree Protocol (RSTP)
Describe how and where to configure the following features: PortFast, UplinkFast, BackboneFast, BPDU Guard, BPDU Filter, Root Guard, Loop Guard, Unidirectional Link Detection, and FlexLinks
Configure Multiple Spanning Tree (MST)
Troubleshooting STP
Notes: Chapter 1 Objectives

## Slide 3: Spanning Tree Protocol Overview

## Slide 4: Spanning Tree Protocol Overview
Upon completing this section, you will be able to meet these objectives:
Explain the need for STP
List different standards of STP
Describe basic STP operation
Describe bridge protocol data units
Explain the root bridge election
Explain the root port election
Explain designated port election
Explain STP port states
Explain PVST+
Explain STP topology changes

## Slide 5: STP Need
Redundant topology can eliminate single points of failure in the network , however, STP blocks certain ports, so there is only one active path to each segment .

## Slide 6: Redundant Topology Problems
Broadcast storms
  Each switch on a redundant network floods broadcast frames endlessly. These frames then travel around the loop in all directions.
Multiple frame transmission
  Multiple copies of the same unicast frames may be delivered to destination station, which can cause problems with the receiving protocol. Multiple copies of the same frame can cause unrecoverable errors.
MAC database instability
  If a loop occurs, the same source MAC address could be seen on multiple interfaces causing instability. Data forwarding can be impaired when the switch consumes the resources that are coping with instability in the MAC address table.

## Slide 7: Solution
STP allows physical path redundancy while preventing the undesirable effects of active loops in the network.
STP forces certain ports into a standby state so that they do not listen, forward, or flood data frames.
There is only one active path to each network segment.
If there is a problem with connectivity to any of the segments, STP reestablishes connectivity by automatically activating a previously inactive path.
STP uses bridge protocol data units (BPDUs) for its operations.
Notes: BPDUs are messages that STP uses to determine current topology information and how to react if any devices added or removed or changed in the topology. By default they are sent out every 2 seconds on all switch ports. BDPUs are discussed later in detail.

## Slide 8: STP Standards
Notes: ■ STP itself is the original IEEE 802.1D version, which provides a loop-free topology in a network with redundant links. STP was created for a bridged network, so it supports only a single LAN or one VLAN.
■ Common Spanning Tree (CST) assumes one spanning-tree instance for the entire network. Unlike 802.1D, it supports more than one VLAN.
■ PVST and PVST+ are Cisco proprietary protocols that provide a separate spanningtree instance for each VLAN configured in the network. PVST protocol is obsolete.
■ MST maps multiple VLANs into the same spanning-tree instance. MST was defined based on the Cisco prestandard MST. Cisco switches now use the standard implementation.
■ RSTP is standard, described in IEEE 802.1w. It is an evolution of STP that provides faster convergence of STP.
■ RPVST+ is a Cisco implementation of RSTP that is based on PVST+.

## Slide 9: STP Operations
STP provides loop resolution by managing the physical path to the given network segment, by performing the following three steps:
1. Elects one root bridge
  Only one bridge can act as the root bridge. The root bridge is the reference point; all data flows in the network are from the perspective of this switch. All ports on a root bridge are forwarding traffic.
2. Selects the root port on the nonroot bridge
  One port on each nonroot bridge I the root port. It is the port with the lowest-cost path from the nonroot bridge to the root bridge. By default, STP path cost is calculated from the bandwidth of the link. You can also set STP path cost manually.
3. Selects the designated port on each segment
  There is one designated port on each segment. It is selected on the bridge with the lowest-cost path to the root bridge.

## Slide 10: STP Operations

## Slide 11: STP Port Roles

## Slide 12: Bridge Protocol Data Units
STP uses BPDUs to exchange STP information, specifically for root bridge election and for loop identification.
By default, BPDUs are sent out every 2 seconds.
BPDUs are generally categorized into two types:
  Configuration BDPUs
    Used for calculating the STP
  TCN (topology change notification) BPDUs
    Used to inform changes in the network topology

## Slide 13: The BPDU Frame
Protocol ID: Identifies the STP
Version: Identifies the current version of the protocol
Message Type: Identifies the type of BPDU (configuration or TCN BPDU)
Flags: Used in response to a TCN BPDU
Root Bridge ID: Identifies the bridge ID (BID) of the root bridge
Root Path Cost: Identifies the cost from the transmitting switch to the root
Sender Bridge ID: Identifies the BID of the transmitting switch
Port ID: Identifies the transmitting port
Message Age: Indicates the age of the current BPDU
Max Age: Indicates the timeout value
Hello Time: Identifies the time interval between generations of configuration BPDUs by the root
Forward Delay: Defines the time a switch port must wait in the listening and learning state

## Slide 14: Root Bridge Election
The root bridge is chosen with an election.
In STP, each switch has a unique BID that consists of the following:
  Bridge priority (a value between 0 and 65,535, with the default being 32,768)
  MAC address
The root bridge is selected based on the lowest BID.
If all switches in the network have the same priority, the switch with the lowest MAC address becomes the root bridge

## Slide 15: Root Port Election
After the root bridge is elected, each nonroot bridge must figure out where it is in relation to the root bridge.
Root port is the port with the best path to the root bridge.
To determine root ports on nonroot bridges, cost value is used.
The path cost is the cumulative cost of all links to the root bridge.
Root port indicates the lowest cost to the root bridge.
Notes: Note Bandwidth of the EtherChannel is calculated as the sum of all the links that are bundled into the EtherChannel. The cost of the EtherChannel link is calculated based on the summed bandwidth.
When two ports have the same cost, arbitration can be done using the advertised port ID (from the neighboring switch).
Note Remember that the port ID’s selection is based on the port ID of the advertised neighboring switch.

## Slide 16: Designated Port Election
After the root bridge and root ports on nonroot bridges have been elected, to prevent the loops STP has to identify which port on the segment will forward the traffic.
Only one of the links on a segment should forward traffic to and from that segment.
The designated port, the one forwarding the traffic, is also chosen based on the lowest cost to the root bridge.
On the root bridge, all ports are designated.
If there are two paths with equal cost to the root bridge, STP uses the following criteria for best path determination and consequently for determination of designated and nondesignated ports on the segment:
  Lowest root BID
  Lowest root path cost to root bridge
  Lowest sender BID
  Lowest sender port ID

## Slide 17: STP Process
Notes: Explain everything

## Slide 18: STP Port States
Notes: ■ Blocking: In this state, the port ensures that no bridging loops occur. A port in this state cannot receive or transmit data, but it receives BPDUs, so the switch can hear from its neighbor switches and determine the location, and root ID, of the root switch and port roles of each switch. A port in this state is a nondesignated port, and therefore it does not participate in active topology.
■ Listening: A port is moved from blocking to listening state if there is a possibility to be selected as the root or designated port. The port in this state still cannot send or receive data frames. But it is allowed to send and receive BPDUs, so it is participating in active topology.
■ Learning: After a period of time (forward delay) in listening state, the port is moved to learning state. The port still sends and receives BPDUs; in addition, it can learn and add new MAC addresses to its table. A port in this state cannot send any data frames.
■ Forwarding: After another period of time (forward delay) in learning state, the port is moved to forwarding state. It is considered as part of the active topology. It sends and receives frames and also sends and receives BPDUs.
■ Disabled: In this state, a port is administratively shut down. It does not participate in spanning tree, and it does not forward frames.

## Slide 19: Per-VLAN STP Plus (PVST+)
Per-VLAN STP Plus (PVST+) is a Cisco implementation of STP that provides a separate spanning-tree instance for each configured VLAN in the network.
Notes: Note PVSTP+ is usually the default STP on Cisco switches.

## Slide 20: Per-VLAN STP Plus (PVST+)
Spanning-tree operation requires that each switch has a unique BID.
To carry BID information, the extended system ID is accommodated.
The original 16-bit bridge priority field is split into two fields, resulting in the following components in the BID:
Bridge priority
  A 4-bit field used to carry bridge priority. The default priority is 32,768, which is the midrange value. The priority is conveyed in discrete values in increments of 4096.
Extended system ID
  A 12-bit field carrying the VLAN ID.
MAC address
  A 6-byte field with the MAC address of the switch.

## Slide 21: STP Topology Changes

## Slide 22
Rapid Spanning Tree Protocol

## Slide 23: Rapid Spanning Tree Protocol
Upon completing this section, you will be able to meet these objectives:
List and explain RSTP port roles
Compare RSTP and STP port states
Explain how STP handles topology changes
Describe RSTP link types
Configure and modify STP behavior
Explain how RSTP handles topology changes

## Slide 24: RSTP Port Roles
RSTP defines the following port roles :
Root
  The root port is the switch port on every nonroot bridge that is the chosen path to the root bridge.
  There can be only one root port on every switch.
  The root port is considered as part of active topology.
  It forwards, sends, and receives BPDUs (data messages).
Designated
  Each switch has at least one switch port as the designated port for the segment.
  In active topology, the switch with the designated port receives frames on the segment that are destined for the root bridge.
  There can be only one designated port per segment.

## Slide 25: RSTP Port Roles
RSTP defines the following port roles :
Alternate
  The alternate port is a switch port that offers an alternate path toward the root bridge.
  It assumes a discarding state in an active topology.
  The alternate port makes a transition to a designated port if the current designated path fails.
Disabled
  A disabled port has no role within the operation of spanning tree.
Backup
  The backup port is an additional switch port on the designated switch with a redundant link to the shared segment for which the switch is designated.
  The backup port has the discarding state in active topology.

## Slide 26: RSTP Port Roles

## Slide 27: Comparison of RSTP and STP Port States

## Slide 28: RSTP Ports States

## Slide 29: RSTP Topology Changes
With RSTP, the TC propagation is now a one-step process. In fact, the initiator of the topology change floods this information throughout the network, as opposed to 802.1D, where only the root did.
This mechanism is much faster than the 802.1D equivalent.
In just a few seconds, or a small multiple of hello times, most of the entries in the CAM tables of the entire network (VLAN) flush.
Why does RSTP not consider link failure a topology change?
  Loss of connectivity does not provide new paths in topology. If a switch loses the link to a downstream switch, the downstream switch either has an alternate path to the root bridge or it does not.
  If the downstream switch has no alternate path, no action will be taken to improve convergence.
  If the downstream switch has an alternate path, the downstream switch will unblock it and consequently generate its own BPDUs with the TC bit set.
  Like with STP, PortFast-enabled ports do not create topology changes.
Notes: When a switch receives a BPDU with TC bit set from a neighbor, it clears the MAC addresses learned on all its ports except the one that receives the topology change.
The switch also receives BPDUs with the TC bit set on all designated ports and the root port.
RSTP no longer uses the specific TCN BPDUs unless a legacy bridge needs to be notified.

## Slide 30: Configuring and Modifying STP Behavior

## Slide 31: Changing STP Priority
It is not advised for the network to choose the root bridge by itself. If all switches have default STP priorities, the switch with the lowest MAC address will become the root bridge.
The oldest switch will have the lowest MAC address because the lower MAC addresses were factory-assigned first.
To manually set the root bridge, you can change a switch’s priority
Note
  It is highly recommended to configure the distribution or core switches to become the root bridge.

## Slide 32: Changing STP Priority
The priority can be a value between 0 and 65,535, in increments of 4096. The default value is 32,768.
The better solution is to use spanning-tree vlan vlan-id root { primary | secondary } command.
This command is actually a macro that lowers the switch’s priority number for it to become the root bridge.
To configure the switch to become the root bridge for a specified VLAN, use the primary keyword.
Use the secondary keyword to configure a secondary root bridge.
The spanning-tree root command calculates the priority by learning the current root priority and lowering the 4096 value to it.
Notes: Note If the priority of the root bridge is set to 0, configuring another switch with the root primary command will yield no results. The command will fail because it cannot make a local switch priority for 4096 lower than that of the root bridge.

## Slide 33: STP Path Manipulation

## Slide 34: STP Path Manipulation
You can modify port cost by using the spanning-tree vlan vlan-list cost cost-value command.
The cost value can be between 1 and 65,535.
You can modify the port priority by using the spanning-tree vlan vlan-list port-priority port-priority command. The value of port priority can be between 0 and 255; the default is 128.
A lower port priority means a more preferred path to the root bridge.

## Slide 35: STP Timers
STP uses three different timers to ensure proper loop-free convergence. The three key STP timers and their default values are as follows:
Hello time
  The time between each BPDU that is sent on a port. Equals 2 seconds, by default.
Forward delay
  The time that is spent in the listening and learning state. Equals 15 seconds, by default.
Max (maximum) age
  Controls the maximum length of time that passes before a bridge port saves its configuration BPDU information. Equals 20 seconds, by default.

## Slide 36: STP Timers
The transition between port states takes from 30 to 50 seconds, depending on the topology change.
This can be adjusted with STP timers. STP hello time can be tuned between 1 and 10 seconds, forward delay between 4 and 30 seconds, and maximum age between 6 and 40 seconds.
To manually configure timers, use the spanning-tree [ vlan vlan-id ] { hello-time | forward-time | max-age } seconds command.

## Slide 37: Changing the STP Mode to RSTP
The convergence time for RSTP is much shorter than for STP. The entire convergence happens at the speed of BPDU transmission.
That can be less than 1 second.

## Slide 38
Implementing STP Stability Mechanisms

## Slide 39: Cisco Spanning Tree Protocol Toolkit
Provides tools to better manage STP.
The key features of are as follows:
UplinkFast: Enables fast uplink failover on access switch
BackboneFast: Enables fast convergence in distribution or core layer when STP change occurs
PortFast: Configures access port to transition directly to forwarding state

## Slide 40: Cisco Spanning Tree Protocol Toolkit
The key features of the Cisco STP Toolkit that ensure STP stability are as follows:
BPDU Guard
  Disables the PortFast-enabled port if a BPDU is received
BPDU Filter
  Suppresses BPDUs on ports
Root Guard
  Prevents external switches from becoming roots
Loop Guard
  Prevents an alternate port from becoming the designated port if no BPDUs are received

## Slide 41: Use UplinkFast
If forwarding uplink fails, it will take 30 to 50 seconds for the other uplink to take over.
UplinkFast is a Cisco proprietary solution that greatly reduces convergence time.
The UplinkFast feature is based on the definition of an uplink group. On a given switch, the uplink group consists of the root port and all the ports that provide an alternate connection to the root bridge. If the root port fails, which means if the primary uplink fails, a port with the next lowest cost from the uplink group is selected to immediately replace it.
The total time to recover the primary link failure will normally be less than 1 second.

## Slide 42: Use UplinkFast
UplinkFast is a Cisco proprietary feature
By default, UplinkFast is disabled.
To enable UplinkFast, use the following command:
ASW(config)# spanning-tree uplinkfast
With RSTP, the UplinkFast mechanism is already integrated into the protocol in a standards-based way.

## Slide 43: Use BackboneFast
When an indirect link failure occurs, BackboneFast checks whether an alternative path exists to the root bridge.
Indirect failure is when a link that is not directly connected to a switch fails.
Notes: As shown in Figure 4-19 , DSW3 is the root bridge, and DSW2 is the one blocking DSW3’s alternate path to DSW1. When DSW1’s root port fails, DSW1 declares itself the root bridge and starts sending BPDUs to all switches it is connected to (in this case, only DSW2). These BPDUs are inferior. When a switch receives an inferior BPDU on a blocked port, it runs a procedure to validate that it still has an active path to the currently known root bridge.

## Slide 44: Use BackboneFast
Normally a switch must wait for the maximum age timer to expire before responding to the inferior BPDUs.
However BackboneFast searches for an alternative path:
If the inferior BPDU arrives on a port that is blocked, the switch assumes that the root port and all other blocked ports are an alternative path.
If the inferior BPDU arrives on a port that is root, the switch assumes all blocked are an alternate path.
If no ports are blocked, the switch assumes that it lost connectivity with the root bridge and considers itself as the root bridge.
After the switch identifies potential alternative ports, it starts sending RLQs (request link queries). By sending these queries, it finds out whether upstream switches have a path to the root bridge.
Notes: When a switch, which is either the root bridge or has a connection to the root bridge, receives an RLQ, the switch sends back an RLQ reply. Otherwise, an RLQ gets forwarded until it gets to a switch that is the root bridge or has a connection to the root bridge.
If exchange of RLQ messages results in validation that the root bridge (DSW3) is still accessible, the switch (DSW2) starts sending existing root bridge information to the bridge that lost connectivity through its root port (DSW1). If this validation fails, DSW2 can start the root bridge election process. In either of these cases, if validation is successful or not, maximum age time is shortened.

## Slide 45: Use BackboneFast
To configure BackboneFast, use the following command:
  DSW1(config)# spanning-tree backbonefast
By default, BackboneFast is disabled.
To verify the current BackboneFast state, issue the following command:
  DSW1# show spanning-tree backbonefast
  BackboneFast is enabled
BackboneFast was implemented into RSTP. RSTP implementation differs a bit from BackboneFast. Whereas BackboneFast relies on RLQ messages to validate the current root bridge, RSTP relies on cached information.

## Slide 46: Use PortFast
When PortFast is enabled, the port transitions immediately from blocking to forwarding.
PortFast should be enabled on access layer switches where the hosts are connected.
An additional benefit of using PortFast is that TCN BPDUs are not sent when a switch port in PortFast mode goes up or down.
By default, PortFast is disabled on all switch ports.
You can configure PortFast in two ways: per port and globally.
  If you configure PortFast globally, all ports that are configured as access ports automatically become PortFast enabled, and the port will immediately transition to forwarding.
    If a port does receive a BPDU, that port will go into blocking mode.
  If you configure PortFast per port
    The port will be PortFast enabled even if it receives BPDUs
Notes: NOTA

## Slide 47: Use PortFast

## Slide 48: PortFast Configuration for a Trunk
Never use the PortFast feature on switch ports that connect to other switches, hubs, or routers.
You can also enable PortFast on trunk ports.
This is useful if you have a trunk enabled for a host such as a server that needs multiple VLANs.
To enable a port for PortFast on an interface that connects to such a server, use the following interface configuration commands:
Notes: These connections can cause physical loops, and spanning tree must go through the full initialization procedure in these situations. A spanning-tree loop can bring your network down. If you turn on PortFast for a port that is part of a physical loop, there can be a window of time when packets are continuously forwarded (and can even multiply) in such a way that the network cannot recover.

## Slide 49: Securing PortFast Interface with BPDU Guard
BPDU Guard protects the integrity of ports that are PortFast enabled.
If any BPDU is received on a PortFast-enabled port, that port is put into err-disabled state.
That means the port is shut down and must be manually reenabled or automatically recovered through the error-disabled timeout function.
It is highly recommended to always enable BPDU Guard on all PortFast-enabled ports.

## Slide 50: Securing PortFast Interface with BPDU Guard
By default, BPDU Guard is disabled on all switch ports.
BPDU Guard can be configured in two ways, globally and per port.
Global configuration is conditional: If the port is not PortFast enabled, BPDU Guard will not be activated.

## Slide 51: Disabling STP with BPDU Filter
BPDUs are sent on all ports, even if they are PortFast enabled.
You should always run STP to prevent loops.
However, in special cases, you need to prevent BPDUs from being sent out.
You can achieve that by using BPDU Filter.
Notes: Configuring BPDU Filter so that all configuration BPDUs received on a port are dropped can be useful for service provider environments, where a service provider provides Layer 2 Ethernet access for customers. Ideally, the service provider does not want to share any spanning-tree information with customers, because such sharing might jeopardize the stability of the service provider’s internal spanning-tree topology. By configuring PortFast and BPDU Filter on each customer access port, the service provider will not send any configuration BPDUs to customers and will ignore any configuration BPDUs sent from customers

## Slide 52: Disabling STP with BPDU Filter
BPDU Filter behaves differently if applied globally or on a per-port basis.
When enabled globally, BPDU Filter has these attributes:
  It affects all operational PortFast ports on switches that do not have BPDU Filter configured on the individual ports.
  If BPDUs are detected, the port loses its PortFast status, BPDU Filter is disabled, and the STP sends and receives BPDUs on the port as it would with any other STP port on the switch.
  Upon startup, the port transmits ten BPDUs. If this port receives any BPDUs during that time, PortFast and PortFast BPDU Filter are disabled.
When enabled on an individual port, BPDU Filter has these attributes:
  It ignores all BPDUs received.
  It sends no BPDUs.

## Slide 53: Use Root Guard
The Root Guard feature forces an interface to become a designated port to prevent surrounding switches from becoming a root switch.
In other words, Root Guard provides a way to enforce the root bridge placement in the network.
If the bridge receives superior STP BPDUs on a Root Guard-enabled port, the port moves to a root-inconsistent STP state and the switch does not forward traffic out of that port.

## Slide 54: Use Root Guard
The current design recommendation is to enable Root Guard on all access ports so that a root bridge is not established through these ports.

## Slide 55: Configuring and Verifying Root Guard

## Slide 56: Loop Guard Overview
STP relies on continuous reception or transmission of BPDUs based on the port role.
The designated port transmits BPDUs, and the nondesignated port receives BPDUs.
When one of the ports in a physically redundant topology no longer receives BPDUs, the STP conceives that the topology is loop free.
Eventually, the blocking port from the alternate or backup port becomes designated and moves to a forwarding state.
This situation creates a loop.
The Loop Guard feature makes additional checks. If BPDUs are not received on a nondesignated port, and Loop Guard is enabled, that port is moved into the STP loopinconsistent blocking state, instead of the listening/learning/forwarding state.

## Slide 57: Loop Guard Overview

## Slide 58: Loop Guard Overview
When the Loop Guard blocks an inconsistent port, this message is logged:
Once the BPDU is received on a port in a loop-inconsistent STP state, the port transitions into another STP state. After recovery, this message is logged:

## Slide 59: Loop Guard Placement
The Loop Guard feature is enabled on a per-port basis.
However, as long as it blocks the port on the STP level, Loop Guard blocks inconsistent ports on a per-VLAN basis
By default, Loop Guard is disabled. You can configure Loop Guard globally or on a port-per-port basis.
If you enable Loop Guard globally, then effectively, it is enabled on all point-to-point links.

## Slide 60: Loop Guard vs Root Guard
The Root Guard is mutually exclusive with the Loop Guard.
The Root Guard is used on designated ports, and it does not allow the port to become nondesignated.
The Loop Guard works on nondesignated ports and does not allow the port to become designated through the expiration of maximum age.
The Root Guard cannot be enabled on the same port as the Loop Guard.
When the Loop Guard is configured on the port, it disables the Root Guard configured on the same port.

## Slide 61: Use UDLD
Unidirectional links can cause spanning-tree topology loops.
Unidirectional Link Detection (UDLD) enables devices to detect when a unidirectional link exists and also to shut down the affected interface.
UDLD is useful on a fiber port to prevent network issues resulting in miswiring at the patch panel causing the link to be in up/up status but the BPDUs are lost.

## Slide 62: UDLD Overview

## Slide 63: UDLD Overview
Notes: Both UDLD peers discover each other by exchanging special frames that are sent to well-known MAC address 01:00:0C:CC:CC:CC
In an EtherChannel bundle, UDLD will error-disable only the physical link that has failed.

## Slide 64: UDLD Overview
UDLD is a Layer 2 protocol that works with the Layer 1 mechanisms to determine the physical status of a link.
Both UDLD peers discover each other by exchanging special frames that are sent to well-known MAC address 01:00:0C:CC:CC:CC
In an EtherChannel bundle, UDLD will error-disable only the physical link that has failed.
UDLD messages are sent at regular intervals. This timer can be modified. The default setting varies between platforms. The typical value is 15 seconds.
UDLD is a Cisco proprietary protocol that is also defined in RFC 5171.

## Slide 65: UDLD Operation
After UDLD detects a unidirectional link, it can take two courses of action, depending on configured mode. UDLD has two modes:
Normal mode
  When a unidirectional link is detected, the port is allowed to continue its operation. UDLD just marks the port as having an undetermined state. A syslog message is generated.
Aggressive mode
  When a unidirectional link is detected, the switch tries to reestablish the link. It sends one message a second, for 8 seconds. If none of these messages is sent back, the port is placed in error-disabled state.

## Slide 66: UDLD Configuration
As with other commands, like PortFast, you can enable UDLD on a per-port basis or globally.
It is supported only at the fiber ports.
Use the udld reset command to reset all the interfaces that were shut down by UDLD.

## Slide 67: Comparing Loop Guard with UDLD

## Slide 68: UDLD Recommended Practices
Typically, it is deployed on any fiber-optic interconnection.
Use UDLD aggressive mode for best protection.
Turn on in global configuration to avoid operational errors and misses.

## Slide 69: Use FlexLinks
FlexLinks are a pair of a Layer 2 interfaces, where one interface is configured to act as a backup to the other.
FlexLinks provide link-level redundancy that is an alternative to STP.
STP is automatically disabled on FlexLinks interfaces.

## Slide 70: FlexLinks Configuration and Verification

## Slide 71: FlexLinks Guidelines
You can configure only one FlexLinks backup link for any active link
An interface can belong to only one FlexLinks pair.
Neither of the links can be a port that belongs to an EtherChannel. However, you can configure two port channels as FlexLinks.
A backup link does not have to be the same type (Fast Ethernet, Gigabit Ethernet, or port channel) as the active link.
STP is disabled on FlexLinks ports

## Slide 72: STP Stability Mechanisms Recommendations

## Slide 73: STP Stability Mechanisms Recommendations
PortFast: Apply to all end-user ports. To secure PortFast-enabled ports, always combine PortFast with BPDU Guard.
Root Guard: Apply to all ports where root is never expected.
Loop Guard: Apply to all ports that are or can become nondesignated.
UDLD: The UDLD protocol enables devices to monitor the physical configuration of the cables and detect when a unidirectional link exists..
Depending on the security requirements of an organization, the port security feature can be used to restrict the ingress traffic of a port by limiting the MAC addresses that are allowed to send traffic into the port.
Notes: The use of Root Guard and Loop Guard is mutually exclusive.
Examples where you will need to implement BPDU Filters are rare. Under no circumstances should you use BPDU Filter and BPDU Guard on the same interface.

## Slide 74: Configuring Multiple Spanning Tree Protocol

## Slide 75: Multiple Spanning Tree Protocol 802.1s
The main purpose of MST is to reduce the total number of spanning-tree instances to match the physical topology of the network and thus reduce the CPU cycles of a switch
MST is a concept of mapping one or more VLANs to a single STP instance.
The number of instances of spanning tree is reduced to the number of links that are available.

## Slide 76: VLAN Load Balancing
Two links and 1000 VLANs
The 1000 VLANs map to two MST instances. Rather than maintaining 1000 spanning trees, each switch needs to maintain only two spanning trees, reducing the need for switch resources.
Notes: MST converges faster than PVRST+ and is backward compatible with 802.1D STP, 802.1w (RSTP), and the Cisco PVST+ architecture.

## Slide 77: Introducing MST
MST allows for the building of multiple spanning trees over trunks by grouping and associating VLANs to spanning-tree instances.
Each instance may have a topology that is independent of other spanning-tree instances.
This architecture provides multiple forwarding paths for data traffic and enables load balancing.
A failure in one forwarding path does not affect other instances with different forwarding paths; hence, this architecture improves network fault tolerance.
MST converges faster than PVRST+ and is backward compatible with 802.1D STP, 802.1w (RSTP), and the Cisco PVST+ architecture.

## Slide 78: MST
Benefits
  Load-balancing scheme is still possible because half the VLANs follow one separate instance.
  The switch utilization is low because it has to handle only two instances.
Drawbacks
  The protocol is more complex than the usual spanning tree and therefore requires additional training of the operation staff.
  Interaction with legacy bridges is sometimes challenging.

## Slide 79: MST Regions
MST differs from the other spanning-tree implementations in combining some but not necessarily all VLANs into logical spanning-tree instances.
This difference raises the problem of determining which VLAN is supposed to be associated with which instance.
VLAN-to-instance association is communicated by tagging the BPDUs so that the receiving device can identify the instances and the VLANs to which they apply.
To provide this logical assignment of VLANs to spanning trees, each switch that is running MST in the network has a single MST configuration consisting of following three
  An alphanumeric configuration name (32 bytes)
  A configuration revision number (2 bytes)
  A 4096-element table that associates each of the potential 4096 VLANs supported on the chassis with a given instance

## Slide 80: MST Regions
To be part of a common MST region, a group of switches must share the same configuration attributes.
It is the responsibility of the network administrator to propagate the configuration properly throughout the region.

## Slide 81: MST Regions
The exact VLAN-to-instance mapping is not propagated in the BPDU because the switches need to know only whether they are in the same region as a neighbor.
Therefore, only a digest of the VLAN-to-instance mapping table is sent, along with the revision number and the name.
After a switch receives a BPDU, it extracts the digest and compares it with its own computed digest.
If the digests differ, the mapping must be different, so the port on which the BPDU was received is at the boundary of a region.
Notes: Digest (a numeric value derived from the VLAN-to-instance mapping table through a mathematical
function)

## Slide 82: MST Configuration Revision
The configuration revision number gives you a method of tracking changes that are made to the MST region.
It does not automatically increase each time that you make changes to the MST configuration.
Each time that you make a change, you should increase the revision number by one.

## Slide 83: STP Instances with MST
MST supports a number of instances.
Instance 0 is the internal spanning tree (IST).
Notes: MST does not send BPDUs for every active STP instance separately. A special instance (instance 0) is designed to carry all STP-related information. BPDUs carry all the usual STP information, in addition to configuration name, revision number, and hash value that is calculated over VLAN-to-instance mapping tables. If hash values do not match, an MST misconfiguration exists between the two switches.
Figure 4-36 shows how different MST instances (MSTIs) exist within a single MST region. MSTI1 and MSTI2 are mapped to different VLANs. Their topologies converge differently because root bridges are configured differently. Within the MST region, there are three independent STP instances: MSTI0 (IST), MSTI1, and MSTI2.

## Slide 84: STP Instances with MST
All six VLAN instances initially belong to MSTI0. This is the default behavior.
Then make the half of VLAN instances (11, 22, and 33) mapped to MSTI1, and the other half (44, 55, and 66) mapped to MSTI2.
If different root bridges are configured for MSTI1 and MSTI2, their topologies will converge differently.
By having different Layer 2 topologies between MST instances, links are more evenly utilized.

## Slide 85: STP Instances with MST
Within a topology where multiple variations of STP are used, Common Spanning Tree (CST) topology considers an MST region as a single black box.
CST maintains a loopfree topology with the links that connect the regions to each other and to switches that are not running MST
Notes: Within the MST region, the IST instance maintains a loop-free topology. IST presents the whole MST region as a single virtual bridge to the outside STP. BPDUs between the MST’s STP instance and the CST’s STP instance are exchanged over the native VLAN, as if a single CST were used.

## Slide 86: Extended System ID for MST
As with PVST, the 12-bit Extended System ID field is used in MST.
In MST, this field carries the MST instance number.

## Slide 87: Configuring and Verifying MST

## Slide 88: Configuring MST with the CCNP Region

## Slide 89: MST Instance 1 and 2 Configuration
MST is configured with three instances.
VLANs 2 and 3 belong to instance 1.
VLANs 4 and 5 belong to instance 2.
All other VLANs between 1 and 4094, that are not in instances 1 or 2, belong to instance 0.
Notes: Using the end or exit command will apply configuration. If you want to abort the change use the abort keyword.

## Slide 90: SPT Root Bridge Configuration
Notes: In this example, you have changed the MST switch priority using spanning-tree mst instance-id root {primary | secondary}. This command is actually a macro that sets the switch’s MST priority, which is a number. If you issue a show running-config, you will see switch priority as a number, not the primary or secondary keyword
Changing STP mode to MST before doing the actual VLAN-to-instance mappings is not advisable. Every change in the mapping will result in recalculation of the STP tree.
A switch cannot run MST and PVST+ at the same time.

## Slide 91: Verifying MST
Notes: To verify currently applied MST configuration, use show current under MST configuration mode. To verify pending MST configuration, use show pending under MST configuration mode. When you type exit or end, pending configuration will become current. So, show current and show pending will produce the same outputs.

## Slide 92: Verifying MST Digest
Notes: The Pre-std Digest refers to Cisco’s legacy prestandard implementation of MST. Cisco developed a proprietary version of MST before MST was released called MISTP , which has similar principles as MST.

## Slide 93: Verifying MST Instances Mappings

## Slide 94: Configuring MST Path Cost
Path cost functions the same as with other STPs, except with MST port costs are configured per instance.

## Slide 95: Configuring MST Port Priority
Port priority functions the same as with other STPs, except with MST port priorities are configured per instance.

## Slide 96: MST Protocol Migration
Ensure that all switch-to-switch links on which a rapid transition is desired are full duplex.
Edge ports are defined through the PortFast feature.
Carefully decide how many instances are needed in the switched network, and keep in mind that an instance translates to a logical topology.
Decide what VLANs to map onto those instances, and carefully select a root and a backup root for each instance.
Choose a configuration name and a revision number that will be common to all switches in the network.
  Cisco recommends that you place as many switches as possible into a single region; it is not advantageous to segment a network into separate regions.

## Slide 97: MST Protocol Migration
Avoid mapping any VLANs onto instance 0.
Migrate the core first. Change the STP type to MST, and work your way down to the access switches.
The configuration of the features such as the PortFast, BPDU Guard, BPDUF Filter, Root Guard, and Loop Guard are also applicable in MST mode.
If you have already enabled these features in the PVST+ mode, it remains active after the migration to MST mode.

## Slide 98: Chapter 4 Summary
Spanning Tree Protocol (STP) overview, its operations, and history
Implement Rapid Spanning Tree Protocol (RSTP)
Describe how and where to configure the following features: PortFast, UplinkFast, BackboneFast, BPDU Guard, BPDU Filter, Root Guard, Loop Guard, Unidirectional Link Detection, and FlexLinks
Configure Multiple Spanning Tree (MST)
Troubleshooting STP

## Slide 99: Chapter 4 Labs
CCNPv7.1 SWITCH Lab4.1 STP
CCNPv7.1 SWITCH Lab4.2 MST

## Slide 101: Acknowledgment
Some of the images and texts are from Implementing Cisco IP Switched Networks (SWITCH) Foundation Learning Guide: (CCNP SWITCH 300-115) by Richard Froom and Erum Frahim (1587206641)
Copyright © 2015 – 2016 Cisco Systems, Inc.
Special Thanks to Bruno Silva